Pasted text(1).txt
Document
Pasted text.txt
Document

cd ~/linux-80211n-csitool-supplementary/injection ./random\_packets

nmcli device status iw dev cat /sys/module/iwlwifi/parameters/debug

cd ~/linux-80211n-csitool-supplementary/injection sudo systemctl stop NetworkManager sudo pkill \-f 'wpa\_supplicant|dhclient|random\_packets' || true mount | grep \-q "on /sys/kernel/debug type debugfs" || sudo mount \-t debugfs none /sys/kernel/debug lsmod | grep \-q '^iwlwifi' || sudo modprobe iwlwifi debug\=0x40000 sleep 1 iw dev

cd ~/linux-80211n-csitool-supplementary/injection sudo ip link set mon0 down 2\>/dev/null || true sudo iw dev mon0 del 2\>/dev/null || true sudo ip link set wlp3s0 down sudo iw dev wlp3s0 set type monitor sudo ip link set wlp3s0 name mon0 sudo iw dev mon0 set channel 36 HT20 sudo ip link set mon0 up iw dev sudo find /sys/kernel/debug \-name monitor\_tx\_rate

gandu, dekh ki dis output

cd ~/linux-80211n-csitool-supplementary/injection ./injector\_prepare\_36ht20.sh

cd ~/linux-80211n-csitool-supplementary/injection ./injector\_prepare\_36ht20.sh ./injector\_send.sh 0x4101 1000 100 1 1000 ./injector\_send.sh 0x4101 5000 100 1 1000 ./injector\_cleanup.sh

This is the ax210 side terminal output while I run this commands from the injector pc terminal

This is my ax210 terminal

Good. The 36/5180/HT20 injector path is confirmed working on the 5300 side.
Since AX210 still saw zero packets there, doing one last controlled try on channel 1 / 2.4 GHz / HT20 is reasonable.
Use this exact variant.
## Prepare on channel 1 / 2412 / HT20
Create a separate script so you don’t disturb the working 36-profile.
cd ~/linux-80211n-csitool-supplementary/injection
cat > injector_prepare_ch1_ht20.sh <<'EOF'
#!/usr/bin/env bash
set -euo pipefail
MON="${1:-mon0}"
echo "[1/7] Stop services/processes that may touch Wi-Fi"
sudo systemctl stop NetworkManager || true
sudo pkill -f 'wpa_supplicant|dhclient|random_packets' || true
echo "[2/7] Ensure debugfs is mounted"
mount | grep -q "on /sys/kernel/debug type debugfs" || sudo mount -t debugfs none /sys/kernel/debug
echo "[3/7] Load iwlwifi in injector mode if needed"
lsmod | grep -q '^iwlwifi' || sudo modprobe iwlwifi debug=0x40000
sleep 1
echo "[4/7] Remove stale interfaces"
sudo ip link set "$MON" down 2>/dev/null || true
sudo iw dev "$MON" del 2>/dev/null || true
sudo ip link set wlp3s0 down 2>/dev/null || true
sudo iw dev wlp3s0 del 2>/dev/null || true
echo "[5/7] Detect PHY"
PHY="$(iw phy | awk '/Wiphy/ {print $2; exit}')"
if [ -z "${PHY:-}" ]; then
    echo "[ERROR] No PHY found"
    exit 1
fi
echo "[INFO] PHY=$PHY"
echo "[6/7] Create monitor interface directly from PHY"
sudo iw phy "$PHY" interface add "$MON" type monitor
echo "[7/7] Tune to channel 1 / 2412 MHz / HT20"
sudo ip link set "$MON" up
sudo iw dev "$MON" set freq 2412 HT20
echo
echo "[INFO] Current interface state:"
iw dev
echo
echo "[INFO] monitor_tx_rate path:"
sudo find /sys/kernel/debug -name monitor_tx_rate
echo
echo "[OK] Injector ready on channel 1 / 2412 MHz / HT20"
EOF
chmod +x injector_prepare_ch1_ht20.sh
## Verify prepare
Run:
cd ~/linux-80211n-csitool-supplementary/injection
./injector_prepare_ch1_ht20.sh
iw dev
You want iw dev to show:
- Interface mon0
- type monitor
- channel 1 (2412 MHz)
- width: 20 MHz
## Send a smoke burst
Use your existing send script:
./injector_send.sh 0x4101 1000 100 1 1000
Then a bigger burst:
./injector_send.sh 0x4101 10000 100 1 500
## AX210 side for this test
Set AX210 to:
- channel 1
- 2412 MHz
- HT20 / 20 MHz
Then test with:
sudo timeout 20 tcpdump -i mon1 -n -e -vvv -s 0
Start tcpdump first, then send the 10000-packet burst from the injector PC.
## What result means what
If AX210 now sees packets on channel 1, then the problem was likely with the 5 GHz 36-path interoperability, not the whole injector idea.
If AX210 still sees zero packets on channel 1 as well, then that is a much stronger sign that the current 5300 + random_packets path is not producing AX210-decodable over-the-air frames for your experiment.
## Cleanup after the test
./injector_cleanup.sh
Run the prepare script and paste just these two outputs:
./injector_prepare_ch1_ht20.sh
iw dev
and after the AX210 test, tell me whether tcpdump stayed at zero or not.
try in 2300MHz
2300 MHz won’t work for this setup.
Why:
- Standard Wi-Fi channels for 2.4 GHz are around 2412–2472 MHz.
- 2300 MHz is not a normal 802.11 Wi-Fi center frequency for your Intel 5300 / AX210 setup.
- So with the current Wi-Fi toolchain, 2300 is not a valid target like 2412 HT20 or 5180 HT20.
For your “last 2.4 GHz try,” use one of these real Wi-Fi frequencies instead:
- 2412 MHz = channel 1
- 2437 MHz = channel 6
- 2462 MHz = channel 11
The best first test is still:
- channel 1
- 2412 MHz
- HT20
If you want, run this on the injector PC:
cd ~/linux-80211n-csitool-supplementary/injection
./injector_prepare_ch1_ht20.sh
iw dev
./injector_send.sh 0x4101 10000 100 1 500
And on the AX210 side, lock it to:
- 2412 MHz
- HT20
If you want to check what your card actually supports, run:
iw list | sed -n '/Band 1:/,/Band 2:/p'
That will show the valid 2.4 GHz channels/frequencies.
gait_project_story (1).docx
Document
I want to setup PicoScene with 5300 for controlled injector for ax210. I already have prepared my ax210 with PicoScene with monitor mode logger.I included the ax210 setup story. I will run it in the pro mode in business subcription. The setup should be very precise and workable. intel 5300 as injector intel ax210 as receiver (already sutup done in Picoscene -- included the doc) Create me the detailed prompt.
Here’s a copy-paste prompt you can use in a new chat.
I built it around your real AX210 workflow: continuous PicoScenes logging, monitor-mode capture, timestamp-based trial extraction/export, CSV plus per-trial .csi, metadata indexing, and the fact that AX210 only captures CSI properly when tuned to the same channel as the traffic of interest. Your current pipeline is already operational, and your remaining bottleneck is standardizing the traffic-generation protocol so packet arrival is more controlled and repeatable.
It also reflects the official PicoScenes docs that say PicoScenes supports IWL5300 and AX210/AX200, supports hardware interoperability among heterogeneous hardware, and describes packet injection-monitor mode as the convenient CSI measurement mode for IWL5300, prepared via array_prepare_for_picoscenes.
I want you to act as a senior Wi-Fi CSI systems engineer, PicoScenes deployment architect, and experimental protocol designer.
I need you to help me design a PRECISE, WORKABLE, LOW-RISK setup plan for using:
- Intel 5300 as the transmitter / controlled injector
- Intel AX210 as the receiver
- PicoScenes as the main software framework
Important: do not treat this as a fresh beginner install problem. Continue from my REAL current state and design a robust migration / integration plan.
==================================================
1. MY REAL CURRENT STATE
==================================================
I am working on a Wi-Fi CSI gait recognition thesis.
My AX210 side is already working in PicoScenes.
The AX210 side is NOT the problem anymore.
My current AX210 receiver workflow already has these properties:
- Ubuntu laptop with Intel AX210
- PicoScenes-based monitor-mode logging already working
- Continuous PicoScenes session model
- Trial-based export workflow already built
- GUI-controlled trial collection workflow already built
- Timestamp-based start/stop marking already built
- Timestamp-based per-trial slicing/export already working
- Per-trial CSV export already working
- Per-trial .csi export already working
- Metadata indexing already working
- The collection GUI has already been refined with subject/trial metadata, operator-friendly logs, and structured output folders
Important known AX210 facts from my existing work:
- AX210 only captures CSI correctly when monitor mode is tuned to the same channel as the traffic of interest
- My collection pipeline depends on correct monitor-interface creation, channel forcing, and verification
- I already understand that passive monitor-mode collection causes packet-count variation
- The main remaining methodological issue is making the traffic source more controlled and repeatable
My current AX210 collection story / architecture summary:
- continuous session logging
- trial start/stop timestamps
- safe timestamp-based slicing instead of unsafe byte slicing
- metadata-driven collection, not just file-name-driven collection
- per-trial CSV + per-trial .csi exports
- GUI-centered trial workflow
So: AX210 receiver side is already established. Do NOT redesign it from scratch unless absolutely necessary.
==================================================
2. WHAT I WANT TO DO NOW
==================================================
I now want to try ONE LAST SERIOUS PATH:
Use PicoScenes with Intel 5300 as the controlled injector / transmitter,
while keeping Intel AX210 as the receiver.
I want to know whether PicoScenes can make the Intel 5300 work better as a controlled injector for the AX210 than the older linux-80211n-csitool supplementary injection path did.
I am NOT asking for a vague feasibility discussion.
I want an implementation-grade plan.
==================================================
3. IMPORTANT OFFICIAL FACTS YOU SHOULD USE
==================================================
Please incorporate and reason from the official PicoScenes documentation, including these facts:
- PicoScenes supports commercial Wi-Fi NICs including Intel AX210/AX200 and Intel 5300
- PicoScenes documents hardware interoperability among heterogeneous hardware
- PicoScenes utility docs say that for IWL5300, a convenient CSI measurement mode is packet injection-monitor mode
- PicoScenes provides utility scripts such as array_prepare_for_picoscenes
- PicoScenes has an IWL5300 frontend in its API documentation
- PicoScenes installation/upgrade workflow is currently documented through the official updater / maintainer path
But do NOT blindly assume that “supported” means “will definitely work for my exact 5300→AX210 controlled injection use case.”
I want you to distinguish very carefully between:
- officially documented support
- likely engineering interpretation
- things that still need proof by experiment
==================================================
4. MY TOOLCHAIN HISTORY THAT YOU MUST RESPECT
==================================================
I have already done substantial work with:
- Intel 5300 old CSI toolchain
- AX210 PicoScenes receiver workflow
- monitor-mode alignment
- packet logging
- metadata-driven trial collection
- GUI-based control
I previously got the old Intel 5300 injection path to the point where:
- the injector scripts ran
- monitor_tx_rate existed
- random_packets transmitted from the 5300 side
- I even got 5300 to a tuned state such as channel 36 / 5180 MHz / HT20 on the injector side
BUT:
- the AX210 still did not decode visible packets from that old injector path
- tcpdump / monitor checks on AX210 saw zero packets during the 5300 random_packets bursts
- so the old supplementary injector path is not yet experimentally validated for my AX210 workflow
That is exactly why I now want to try PicoScenes with 5300 as injector:
to see whether PicoScenes gives a better / cleaner / more interoperable transmitter path than the old 5300 injection tooling.
==================================================
5. MY ENVIRONMENT / CONSTRAINTS
==================================================
Please assume these constraints unless you explicitly justify changing them:
- AX210 receiver stays in PicoScenes
- AX210 receiver workflow is already basically done
- Intel 5300 is the side I want to rework into a controlled injector using PicoScenes if possible
- I want correctness, reproducibility, low risk, and operator clarity
- I do not want shallow advice
- I do not want “just try random stuff”
- If a separate install / separate OS / separate partition / separate boot image is safer, say so clearly and justify it
- If the current 5300 Ubuntu / kernel environment is too old or too incompatible for current PicoScenes, say so clearly
- If I need to stop trying to reuse the old 5300 collector OS and instead make a clean PicoScenes-specific 5300 injector environment, say so clearly
- If current official PicoScenes installation docs target Ubuntu 22.04 or a newer environment, explain the implication for my existing 5300 setup
- Be explicit about whether the safest route is:
  A. reuse current 5300 OS
  B. dual-boot or separate install for PicoScenes-on-5300
  C. stop using 5300 and switch to AX210/AX200 as transmitter instead
==================================================
6. WHAT I NEED YOU TO DELIVER
==================================================
Please structure your answer exactly like this:
SECTION A — Restate my real setup correctly
- Summarize my AX210 receiver workflow correctly
- Summarize my 5300 situation correctly
- Summarize why I am trying PicoScenes with 5300 now
- Show clearly that you understand this is NOT a fresh-start problem
SECTION B — Hard feasibility judgment
Give me your best technical judgment:
- Can PicoScenes with Intel 5300 realistically be used as a controlled injector for my AX210 receiver workflow?
- Is this likely to work better than the old random_packets / lorcon-old path?
- What is officially documented?
- What is only inferred?
- What remains uncertain and must be experimentally validated?
SECTION C — Best architecture choice
Choose the best architecture among these and justify it carefully:
1. Reuse my current 5300 OS and install PicoScenes there
2. Create a separate clean PicoScenes-only 5300 injector environment
3. Abandon 5300-as-injector and use a different transmitter strategy
If you recommend option 2 or 3, say so firmly and explain why.
SECTION D — Exact installation / migration plan for 5300 PicoScenes injector
If you think PicoScenes with 5300 is worth trying, give me the full implementation plan:
- OS recommendation
- kernel recommendation
- whether to preserve or isolate the old collector environment
- exact installation sequence
- official PicoScenes installation steps
- any 5300-specific caveats
- how to verify that PicoScenes sees the IWL5300 device
- how to verify monitor mode / packet-injection readiness
- how to verify frequency/channel/HT20 settings
- how to verify Tx path really exists
SECTION E — Exact receiver/transmitter alignment plan
Design the clean alignment protocol between:
- 5300 PicoScenes injector
- AX210 PicoScenes receiver
Include:
- how channel/frequency/bandwidth should be declared on both sides
- whether channel should be specified by frequency or Wi-Fi channel number
- whether HT20 / HT40 should be used first
- how to keep both sides verifiably aligned
- how to check alignment before every trial
SECTION F — Exact transmitter validation ladder
I need a step-by-step validation plan from lowest risk to full experiment.
Example of the style I want:
1. device detection
2. monitor mode readiness
3. injection readiness
4. minimal burst
5. receiver sees burst in tcpdump
6. receiver sees burst in PicoScenes logs
7. controlled repeated trial burst
For each step include:
- objective
- exact command(s)
- expected success signal
- failure signal
- what the failure most likely means
- what to do next
SECTION G — Exact commands and scripts
I want actual commands and script structure, not only theory.
Please provide:
- official PicoScenes commands where applicable
- any array_prepare_for_picoscenes usage if relevant
- any verification commands using iw / ip / tcpdump / PicoScenes utilities
- any recommended wrapper scripts
- naming conventions for scripts
- safe cleanup scripts
If current official PicoScenes utilities have replaced older manual steps, prefer the official PicoScenes way.
SECTION H — Controlled traffic protocol design
Design the actual injection protocol for the gait experiment.
Include recommendations for:
- best first test frequency/channel
- best first width
- fixed-rate vs adaptive-rate policy
- burst size
- packet interval
- trial duration strategy
- how to produce repeatable traffic conditions
- how to avoid ambient-traffic ambiguity
- how to prove that AX210 is receiving MY 5300 traffic, not unrelated packets
SECTION I — GUI / automation design
I prefer GUI-driven workflows.
Please tell me whether I should:
- build a new small GUI for the 5300 PicoScenes injector side
- keep it backend-first first and GUI later
- or avoid GUI until the injection path is proven
If you recommend GUI later, define the minimum backend API / script layer that should exist first.
SECTION J — Honest stop/go recommendation
At the end, I want your honest engineering judgment:
- GO: PicoScenes + 5300 is worth trying now
- GO, BUT ONLY in a separate clean environment
- NO-GO: move directly to another transmitter strategy
This final recommendation must be explicit and justified.
==================================================
7. HOW I WANT YOU TO THINK
==================================================
Please do all of the following:
- use official PicoScenes docs and primary sources
- reason carefully instead of hand-waving
- distinguish clearly between documented support and real-world interoperability risk
- optimize for experimental usefulness, not just “software installs successfully”
- assume I care more about a correct answer than an optimistic answer
- assume I am okay with a separate clean install if that is the safer route
- assume I would rather hear “this is likely a dead end” than waste more days
==================================================
8. VERY IMPORTANT OUTPUT STYLE
==================================================
Write the answer like you are advising a research engineer who needs to make the next major decision correctly.
Be:
- concrete
- precise
- cautious
- implementation-oriented
- explicit about risk
- explicit about uncertainty
- explicit about rollback / isolation
Do not give me a shallow overview.
Do not ignore my existing AX210 progress.
Do not assume PicoScenes + 5300 is automatically good just because a doc says “supported.”
Please think carefully and then answer.
A slightly shorter version is possible if you want something more compact for a fresh chat.